## Slide 1: Zynq Architecture -- Extend Embedded System into PL with Vivado
Zynq
Vivado 2015.2 Version

## Slide 2: Outline
PS-PL Interface
PL Clocking Sources
Zynq Resets
Process of adding IP to PL

## Slide 3: PS Components
The Zynq AP SoC processing system consists of the following blocks
  Application processing unit (APU)
  I/O peripherals (IOP)
    Multiplexed I/O (MIO), extended multiplexed I/O (EMIO)
  Memory interfaces
  PS interconnect
  DMA
  Timers
    Public and private
  General interrupt controller (GIC)
  On-chip memory (OCM): ROM and RAM
  Debug controller: CoreSight
Notes: APU vs. CPU(Central Processing Unit)

## Slide 4
Notes: The Snoop Control Unit (SCU) connects one to two Cortex-A9 cores to the memory system through the AXI interfaces.

## Slide 5: The PS and the PL
The Zynq-7000 AP SoC architecture consists of two major sections
  PS: Processing system
    Dual ARM Cortex-A9 processor based
    Multiple peripherals
    Hard silicon core
  PL: Programmable logic
    Uses the same 7 series programmable logic, based on the following two FPGA fabrics
      Artix™-based devices: Z-7010, Z-7015 and Z-7020 (high-range I/O banks only)
      Kintex™-based devices: Z-7030, Z-7035, Z-7045, and Z-7100 (mix of high-range and high-performance I/O banks)

## Slide 6: PS-PL Interfaces
AXI general-purpose ports (GP0-GP1)
  Two masters from PS to PL
  Two slaves from PL to PS
  32-bit data width
  Conversation and sync to processing system clock domain
Clock and resets
  Four PS clock outputs to the PL with enable control
  Four PS reset outputs to the PL

## Slide 7: PL Clocking Sources
PS clocks
  PS clock source from external package pin
  PS has three PLLs (Phase-Lock-Loop) for clock generation
  PS has four clock ports to PL
The PL has 7 series clocking resources
  PL has a different clock source domain compared to the PS
  The clock to PL can be sourced from external clock capable pins
  Can use one of the four PS clocks as source
Synchronizing the clock between PL and PS is taken care of by the architecture of the PS
PL cannot supply clock source to PS
Notes: The ZYBO provides a 50 MHz clock to the Zynq PS_CLK input, which is used to generate the clocks for each of the PS subsystems. The 50 MHz input allows the processor to operate at a maximum frequency of 650 MHz and the DDR3 memory controller to operate at a maximum of 525 MHz (1050 Mbps).
The ZYBO Base System Design configures the PS to work properly with this input clock, and should be used as a reference when creating custom designs.
The PS has a dedicated PLL capable of generating up to four reference clocks, each with settable frequencies, that can be used to clock custom logic implemented in the PL. Additionally, The ZYBO provides an external 125 MHz reference clock directly to pin L16 of the PL. The external reference clock allows the PL to be used completely in dependently of the PS, which can be useful for simple applications that do not require the processor.

## Slide 8: Zynq Resets
Internal resets
  Power-on reset (POR)
  Watchdog resets from the three watchdog timers
  Secure violation reset
PS resets
  External reset: PS_SRST_B
  Warm reset: SRSTB
PL resets
  Four reset outputs from PS to PL
  FCLK_RESET[3:0]

## Slide 9: Processing System Interconnect (1)
Programmable logic to memory
  Two ports to DDR
  One port to OCM SRAM
Central interconnect
  Enables other interconnects to communicate
Peripheral master
  USB, GigE, SDIO connects to DDR and PL via the central interconnect
Peripheral slave
  CPU, DMA, and PL access to IOP peripherals

## Slide 10: Processing System Interconnect (2)
Processing system master
  Two ports from the processing system to programmable logic
  Connects the CPU block to common peripherals through the central interconnect
Processing system slave
  Two ports from programmable logic to the processing system

## Slide 11: Communicating with PL
Processing system master
  Two ports from the processing system to programmable logic
  Connects the CPU block to common peripherals through the central interconnect
Processing system slave
  Two ports from programmable logic to the processing system
Slave PL peripherals address range
  4000_0000 and 7FFF_FFFF (connected to GP0) and
  8000_0000 and BFFF_FFFF (connected to GP1)
GP0 GP1

## Slide 12: Process of Adding IP to PL
PS functionality can be extended by instantiating peripherals in PL
Adding IP in PL involves
  Enabling interface(s) in PS
  Selecting IP from the IP Catalog and configuring IP for desired functionality
  Connecting the (PL) IP to the PS using IP Integrator
  Assigning address
  Connecting IP ports to ports of other peripherals and/or to external pins
HDL Wrapper is needed for IP Integrator Block
Bitstream must be generated when PL has any IP
The FPGA must be programmed with the generated hardware bitstream before an application can be run

## Slide 13: ARM Cortex-A9 based Embedded System Design Lab2: Adding IPs in PL
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
Memory
GPIO
UART
RS232
DIP Switches
AXI4-Lite
GPIO
Push-Buttons
AXI4-Lite
M_AXI_GP0
PS
PL

## Slide 14: Procedure
Open the project in Vivado
Enable GP0 in PS
Add and configure GPIO peripherals in the system in the IP Integrator
Add external ports
Generate the bitstream and export to SDK
Create a TestApp application in SDK
Verify the functionality in hardware

## Slide 15: Three Major Steps
The GP Master interface of the PS was enabled. GPIO peripherals were added from the IP catalog and connected to the Processing System through the 32b Master GP interface.
The peripherals were configured and external FPGA connections were established. Pin location constraints were made using IP Integrator Automation, and also manually, to connect the peripherals to push buttons and DIP switches.
A TestApp application project was created and the functionality was verified after downloading the bitstream and executing the program.

## Slide 16: Design Example with Switches Connected

## Slide 17: IP Peripherals Included as Source (Free)
Bus and bridge controllers
  AXI to AXI connector
  Local Memory Bus (LMB)
  AXI Chip to Chip
  AHB-Lite to AXI
  AXI4-Lite to APB
  AXI4 to AHB-Lite
Debug cores
  Integrated Logic Analyzer
DMA and Timers
  Watchdog, fixed interval
Inter-processor communication
External peripheral controller Memory and memory controller
High-speed and low-speed communication peripherals
  AXI 10/100 Ethernet MAC controller
  Hard-core tri-mode Ethernet MAC
  AXI IIC
  AXI SPI
  AXI UART
Other cores
  System monitor
  Xilinx Analog-to-Digital Converter (XADC)
  Clock generator, System reset module
  interrupt controller
  Traffic Generator, Performance monitor

## Slide 18: Vivado IP Catalog
Integrated IP Support
  Instant access to IP customization
  Vivado IP GUI look and feel
  Support for Vivado synthesis and implementation
  Selectable IP output products
  Full Tcl support
Notes: Vivado has a unified IP catalog – all IP available in one place. The catalog can be extended through use of additional repositories. IP can be selected in the catalog and customization GUIs launched. IP is then added directly to a Vivado project, or in the case of IP Integrator, added to the diagram. The user can select simulation or implementation files. IP can be accessed and customized entirely from the Tcl console as well.

## Slide 19: IP Cores Included as Evaluation
AXI CAN controller
AXI USB2 device
Video IP
Telecoms/ Wireless IP
Xilinx developed, delivered, and supported
Evaluation IP installs with a 90-day evaluation license

## Slide 20: GP Ports
By default, GP Slave and Master ports are disabled
Enable GP Master and/or Slave ports depending on whether a slave or a master peripheral is going to be added in PL
axi_interconnect block is required to connect IP to a port with different protocols
  Automatically convert Protocols
  Can be automatically added when using Block Automation in IPI

## Slide 21: Configuring GP Ports
Click on the menu or green GP Blocks to configure

## Slide 22: Add IP in the PL
Configure GP ports from PS Customization GUI
PS-PL Configuration
    E.g. Enable M_AXI_GP0/1 or S_AXI_GP0/1
Ports will then be available on Zynq Block Diagram
Connect the added IP to the appropriate port
Assign address to the added IP, if unmapped
Configure the IP, if necessary
Make external connections, if needed
  Add external ports/interfaces if the added IP is interacting with external devices

## Slide 23: Connecting IP
Add IP from the IP Catalog
Click and drag to find connections
Valid connections Highlighted
Designer Assistance, Connection automation
    If Board Support available, IP can be connected to external pins
Or manually create and connect (external) ports

## Slide 24: Designer assistance; Block Automation, Connection Automation
Block, Connection
Can automatically connect IP blocks
Automatically insert required blocks
E.g. Add BRAM; Automation will insert and connect BRAM controller and Reset logic
If Board Support is available, IP can automatically be connected to top level ports

## Slide 25: Assign Addresses
Peripherals in the Zynq™ AP SoC PS have fixed addresses and do not appear in the address map when an IP is added to the system
For PS peripherals Click on the Auto Assign Addresses button
The address will be generated and show the generated addresses of the added IP
The fixed addresses of the configured peripherals of the PS

## Slide 26: Parameterize IP Instances
Double-click or right click the instance and select Customize Block to open the configurable parameters dialog box (refer to the datasheet if needed)
Default values are shown
  Customize the parameters that you want

## Slide 27: Simulation, Synthesis, and Implementation
Simulation is verifying the functionality of the design . There are two kinds of simulation: 1- behavioral (functional) simulation which is done pre-fit (before synthesis) 2- Timing simulation which is done post-fit (after synthesis) to ensure that it has achieved the required timing.
Synthesis is to implement the design by translating the design into a next level of abstraction: from RTL level to gate level.
Implementation is to translate netlist into the placed and routed FPGA design.
From SW designers' view, Simulation process is something like the debugging process, while the Synthesis and implementation process is something like the compile-link-make process. The Synthesis process is the key point of EDA technology, which makes the Automatic process possible.
Notes: In digital circuit design, register-transfer level (RTL) is a design abstraction which models a synchronous digital circuit in terms of the flow of digital signals (data) between hardware registers, and the logical operations performed on those signals. It is usually written in HDL.

## Slide 29: Bitstream Generation
After defining the system hardware, the next step is to create hardware netlists if the system hardware has logic in PL
An HDL wrapper for the block diagram must be generated
  Additional logic can be added to the HDL, or the Processor system can be used as a sub block in a HDL design
The design and block diagram must be open before synthesise and implementation can be carried out
If the system contains hardware in the PL, the bitstream must be generated
The PL (FPGA) must be programmed before application can be downloaded and executed

## Slide 30: Create a TestApp Application in SDK
Export hardware platform to SDK
Create a test application to test the newly added IPs
The FPGA must be programmed with the generated hardware bitstream before an application can be run