## Slide 1: Creating and Adding Custom IP
Zynq
Vivado 2015.2 Version

## Slide 2: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
Create and Package IP
Custom IP
Summary

## Slide 3: Introducing AXI Interconnect Protocol
AXI is a protocol belonging to the ARM AMBA family of microcontroller buses.
The AMBA protocol is an open standard on-chip interconnect specification, allowing the connection and management of many controllers and peripherals in a multi-master design.
The AXI protocol is optimized for FPGA implementation through coordinated development with Xilinx and is used as a means of communication between IP cores of an FPGA design.

## Slide 4: Basic AXI Transaction Channels
Read address channel
Read data channel
Write address channel
Write data channel
Write response channel
Notes:   Non-posted write model
    There will always be a "write response

## Slide 5: All AXI Channels Use A Basic “VALID/READY” Handshake
SOURCE asserts and holds VALID when DATA is available
DESTINATION asserts READY if able to accept DATA
DATA transferred when VALID and READY = 1
SOURCE sends next DATA (if an actual data channel) or deasserts VALID
DESTINATION deasserts READY if no longer able to accept DATA

## Slide 6: AXI4-Lite Slave
AXI4-Lite is a subset of AXI (Full)
  Same channels, but less signals than full interface
5 AXI channels
  Inputs: Write Address, Data; Read Address
  Outputs: Write Response; Read Data
Slave responds to read and write transactions from upstream Master
1 data transfer per transaction
  No burst support
Intended for lower performance peripherals
AXI Interconnect
User IP
AXI Transaction logic
(Ready, Valid, Response)
Write Response
Read Addr
Read Data
Write Data
Write Addr
Registers
led_ip_v1_0.v
led_ip_v1_0_S_AXI.v
lab3_user_logic.v
AXI4-Lite IP (Slave)

## Slide 7: Example – AXI is Connected to Two Slaves: AXI GPIO and AXI BRAM
The AXI interconnect is a slave to the master processing system, and is a master routing signals from the processor to various instances of slave AXI devices. In this system, the interconnect is connected to two slave devices; AXI GPIO (gpio_1) and an AXI BRAM controller (bram_ctrl_1).

## Slide 8: Reusing Your IP
IP from many sources can be packaged and made available in Vivado
All IP available in the Vivado IP Catalog can be used to create IP Integrator designs
Any IP Integrator diagram can be quickly packaged as a single complex IP
IP Packager
Source (C, RTL, IP, etc)
Simulation Models
Documentation
Example Designs
Test Bench
Vivado IP Integrator
Standardized IP-XACT representation
IP Catalog
Xilinx IP
3rd Party IP
User IP
Notes: Vivado supports reuse of IP is by providing users a means to capture their individual IP or IP subsystems and package that IP, and then make the IP available to other users through the Vivado IP catalog. This approach also benefits third party IP providers, who now have a standard way of providing their IP for both evaluation and purchase, and that IP will be visible through the IP Catalog.
Packaging an IP Integrator diagram takes one Tcl command, or several mouse clicks.

## Slide 9: Create and Package IP
The Create and Package IP wizard allows you to
  Create a template for a new peripheral
  Package the current project
    Only available if project is open
  Package an existing project
The packager allows IP to be included in the IP Catalog for distribution
It uses IP-XACT format
Complete set of files included
  Source code, Constraints, Test Benches (simulation files), documentation

## Slide 10: Create Custom IP
Create and Package IP Wizard
Generates HDL template for
  Slave/Master
    AXI Lite/Full/Stream
Optionally Generates
  Software Driver
    Only for AXI Lite and Full slave interface
  Test Software Application
  AXI4 BFM (Bus Function Model) Example to verify functionality of masters and slaves .

## Slide 11: Create Custom IP
Add IP to repository
Edit IP
Verify
  BFM Simulation Example Design
  JTAG

## Slide 12: Generated Template for AXI Lite
HDL implementation of AXI Interface
  32 bit data width
User specifies required number of registers (minimum 4)
Read from/write to Registers implemented
User logic can be easily connected
User logic can be a hierarchical design

## Slide 13: HDL AXI Lite
Connect user logic to registers, or modify design
Address
Register
Data

## Slide 14: Files created
component.xml
  IP XACT description
bd
  Block Diagram tcl file
drivers
  SDK and software files (c code)
  Simple register/memory read/write functionality
  Simple SelfTest() code
hdl
  Verilog/VHDL (should be inside project directory
xgui
  GUI tcl file

## Slide 15: Edit IP
New Vivado project will open
Template files have been generated and are added to the project
IP can now be edited
  Modify existing template files, add user source files
IP Packager will be open
  Last step is to Package IP

## Slide 16: Package IP
Package current project
  Must be open!
  Package generated HDL
Package a directory (another project/source files)
  Option to package as a library core
  Core can be referenced by other IP
  Core not available standalone (Will not display in IP Catalog)
Create New AXI4 Peripheral (previous section)
  Will also need to be packaged
  Similar steps to package for all three flows

## Slide 17
IP Packager
Automatically analyse project/files to determine parameters
Initial Summary
Identifies
  Files
    Source HDL, Testbenches, Documentation,
  Parameters
    Configurable
  Ports
  Interfaces
  Compatibility
Creates GUI Layout for IPI

## Slide 18: IP Packager
Modify configuration
  Properties
  Compatibility
  Files
  Custom parameters
  Ports
  Interfaces
  Address and Memory
  IP and security
Project can be updated – e.g. source files added
  Changes will be reflected in packager
Review and package

## Slide 19: Customizing IP for Reuse in IP Packager
Add, Edit or change defaults
Select
Options
Notes: The packager handles all the IP-XACT specific file creation, manages IP versions, recognizes interfaces, and creates customized configuration dialogs, as well as more advanced functionality.

## Slide 20: IP repository
The Vivado IP Catalog can be extended by adding additional IP Repositories.
Third party IP, your custom IP, and Xilinx IP are displayed in an identical manner
Packager creates .xml file for the IP
Specify the directory of the user/third party IP repository
  Can be done automatically from packager
  Access from project settings, or IP Catalog
  Displays the IP that has been found
Displays IP in the repository for use in IPI

## Slide 21: Summary
AXI4 interface defines five channels
  All channels use basic VALID/READY handshake to complete a transfer
AXI Interconnect extends AXI interface by allowing 1-to-N, N-to-1, N-to-M, and M-to-N connections
Custom IP can be imported using IP Packager
Include in the IP Repository for reuse across projects
Create and Package wizard supports AXI Lite, Full, and Stream compatible IP creation and packaging
  Handles interface side protocol
  Provides template to add HDL functionality
  Packages into the IP Catalog

## Slide 22: Zybo Reference Manual
https://reference.digilentinc.com/reference/programmable-logic/zybo/reference-manual