## Slide 1: Software Development Environment
Zynq
Vivado 2015.2 Version

## Slide 2: Outline
Desktop vs. Embedded
Software Development Tools
Software Development with SDK
Library Generation
Address Management
Linker Script

## Slide 3: Desktop versus Embedded
Desktop development: written, debugged, and run on the same machine
OS loads the program into the memory when the program has been requested to run
Address resolution takes place at the time of loading by a program called the loader
  The loader is included in the OS
The programmer glues into one executable file called ELF
  Boot code, application code, RTOS, and ISRs
  Address resolution takes place during the gluing stage
The executable file is downloaded into the target system through different methods
  Ethernet, serial, JTAG, BDM, ROM programmer

## Slide 4: Embedded versus Desktop
Development takes place on one machine (host) and is downloaded to the embedded system (target)
Host Computer
Target Board
A cross-compiler is run on the host
JTAG
UART

## Slide 5: Embedded Development
Different set of problems
  Unique hardware for every design
  Reliability
  Real-time response requirement (sometimes)
    RTOS versus OS
  Code compactness
  High-level languages and assembly
Notes: Every embedded system design is unique in its function and targeted for a unique application. A design developed for one application may not work for another embedded system. Another issue is reliability. Because the system is standalone, and a combination of hardware and software, the design may have some hidden bugs that can make the system malfunction. Therefore, such a system may not be one hundred percent reliable. Depending on the application, the system may require real-time response and RTOS use, which can lead to bigger code and a larger memory requirement. Real-time systems also require assembly language programming for time-critical applications.

## Slide 6: Software Development Tools

## Slide 7: SDK Application Development Flow

## Slide 8: Launching SDK
Launch SDK
  Standalone
    Choose workspace, choose Hardware Platform Specification
  In Vivado
    File> Export Hardware
    File > Launch SDK
  Exporting
    A Hardware Description File HDF file is first generated
    A hardware platform specification project is then automatically created
      The software application (and board support package) then can be created and associated with the hardware platform

## Slide 9: Creating a Board Support Package
  The Board Support Package provides software services based on the processor and peripherals that make up the processor system
  Can be automatically created when creating Application project
Can be created standalone
Must be attached to a Hardware Platform
  File > New > Board Support Package
  Select appropriate OS support
  Third-party operating systems are supported with the appropriate BSP selection
  Select required libraries support

## Slide 10: Creating a Software Application Project
SDK supports multiple software application projects
A software project is attached to a BSP project
Sample applications are provided
  Great for quick test of hardware
    Peripheral Tests
  Starting point to base your own application on
Typically an Empty Application is opened to begin a non-standard project

## Slide 11
Simulation
Generator
Hardware
Platform Generation
Library Generation
Embedded Software
Development
IP Library or User Repository
MSS
Library Generation
.a
Compiler (GCC)
.o, .a
Linker (GCC)
ELF
IPI
Platform Generation
Drivers
.hdf
HDL
System and Wrapper HDL
system.bmm
Synthesis
Implementation
XDC
Bitstream Generation
system_bd.bmm
Configure BRAM
download.bit
Hardware Manager
system.bit
Simulation model
Generation
Behavioral VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation
IP Models
HDL Models
CompXLib
Application Source .c, .h, .s
Embedded Tool Flow (SDK)
SW Libraries
Libraries,
OS, MLD
XMD, TCF GDB
FPGA
JTAG Cable
Linker Script
SDK

## Slide 12: GNU Tools: GCC
GCC translates C source code into assembly language
GCC also functions as the user interface to the GNU assembler and to the GNU linker, calling the assembler and the linker with the appropriate parameters
Supported cross-compilers:
  GNU GCC (arm-xilinx-eabi-gcc)
Command line only; uses the settings set through the GUI

## Slide 13: GNU Tools: GCC
Calls four different executables
  Preprocessor (cpp0)
    Replaces all macros with definitions defined in the source and header files
  Language specific c-compiler
    cc1 C-programming language
    cc1plus C++ language
  Assembler
    arm-xilinx-eabi-as
  Linker
    arm-xilinx-eabi-ld
arm-xilinx-eabi-as
arm-xilinx-eabi-ld

## Slide 14: GNU Tools: AS
Input: Assembly language files
  File extension: .s
Output: Object code
  File extension: .o
  Contains
    Assembled piece of code
    Constant data
    External references
    Debugging information
Typically, the compiler automatically calls the assembler
Use the -Wa switch if the source files are assembly only and want to use the gcc

## Slide 15: GNU Tools: LD
Linker
Inputs:
  Several object files
  Archived object files (library)
  Linker script (mapfile)
Output:
  Executable image (.ELF)
  Map file

## Slide 16: GNU Utilities
AR Archiver
  Create, modify, and extract from libraries
  Used in SDK to combine the object files of the Board Support Package (BSP) in a library
  Used in SDK to extract object files from different libraries
Object Dump
  Display information from object files and executables
    Header information, memory map
    Data
    Disassemble code
The mb-objdump (powerpc-eabi-objdump) utility lets you see the contents of an object (.o) or executable (.out) file.
To see your symbol table, the size of your file, and the names or sizes of the sections in the file, run:
mb-objdump -x a.out
To see a listing of the (assembly) code in your object or executable file, run:
mb-objdump -d a.out
To get a list of other options, run:
mb-objdump --help
Notes: The mb-objdump (powerpc-eabi-objdump) utility lets you see the contents of an object (.o) or executable (.out) file.
To see your symbol table, the size of your file, and the names or sizes of the sections in the file, run:
mb-objdump -x a.out
To see a listing of the (assembly) code in your object or executable file, run:
mb-objdump -d a.out
To get a list of other options, run:
mb-objdump --help

## Slide 17: Object Dump Display summary information from the section headers
Section
Name
Loadable Memory Address
Virtual Memory Address
Section Size
Byte alignment
Offset from the beginning of the section header table
arm-xilinx-eabi-objdump –h executable.elf

## Slide 18: Object Dump Dumping the source and assembly code
Memory location
C code instruction
Assembly instruction
Machine Language Instruction
arm-xilinx-eabi-objdump –S executable.elf

## Slide 19: Minimal Required Services
C language standard services
  C language construct services
  stdin and stdout
  Math library
  malloc
Processor support requires these services
  Interrupt
  Cache
  Language environment support

## Slide 20: Operating Systems
Operating systems are a collection of software routines that comprise a unified and standard set of system services
The Standalone option is used when no operating system is desired
  Provides a minimal amount of processor and library services as previously illustrated
  Can be considered a minimal, non-standard operating system
  Installed as a software platform
Variety of third-party operating systems are available
  Linux – many flavors
  RTOS – real-time operating system; also has many flavors; Free RTOS (an option for the Cortex™-A9 processor)
  XilKernel – provided by Xilinx; small and simple; only for MicroBlaze
Operating systems are installed and become part of the Board Support Package (BSP)

## Slide 21: What an Operating System Provides?
Operating system services
  GUI support
  TCP/IP services**
  Task management
  Resource management**
  Familiar programming services and tasks
  Easy connection to already written applications
  Ability to reload and change applications
  Full file system services**
  ** Also available as additions to the Standalone BSP

## Slide 22: Do I Need an Operating System?
The Standalone BSP includes the previously discussed items
Design considerations for systems using the Standalone BSP
  All services needed are included in the BSP
  The application is static—it never changes
  The application fits in block RAM (MicroBlaze™ processor), OCM RAM (Zynq™ AP SoC), or DDR memory
  The application is single-task based
  Interrupts may or may not be used

## Slide 23: Accessing Software Platform Properties
Select the created board support package in the Project Explorer view
Xilinx Tools > Board Support Package Settings
Sets all of the software BSP related options in the design
Has multiple forms selection
  Overview
  Standalone
  Drivers
  CPU
As individual Standalone services are selected a configurable menu selection item will appear
Notes: Open the Software Platform Settings dialog box by selecting Tools  Software Platform Settings. This dialog box has multiple forms and is used to set all the software platform-related options in the design.
Overview:
This form allows you to select the OS version and services.
You can also select available libraries support in this form. Depending on the library that you select in this form, a configuration panel menu selection will appear under the Standalone menu.
Standalone:
This form shows a list of all configurable devices (stdin/stdout). You can also select if you want to perform profiling and a timer to be used in profiling. If any library support is selected in the Overview form, and menu of the service’s configurable parameters will be presented under the Standalone menu.
Drivers:
This form allows you to specify values for the parameters associated with the peripheral drivers in the design.
CPU:
Tool chain options and their settings.

## Slide 24
Hardware
Platform Generation
Simulation
Generator
Library Generation
Embedded Software
Development
IP Library or User Repository
MSS
Library Generation
.a
Compiler (GCC)
.o, .a
Linker (GCC)
ELF
IPI
Platform Generation
Drivers
.hdf
HDL
System and Wrapper HDL
system.bmm
Synthesis
Implementation
XDC
Bitstream Generation
system_bd.bmm
Configure BRAM
download.bit
Hardware Manager
system.bit
Simulation model
Generation
Behavioral VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation
IP Models
HDL Models
CompXLib
Application Source .c, .h, .s
Embedded Tool Flow (SDK)
SW Libraries
Libraries,
OS, MLD
XMD, TCF GDB
FPGA
JTAG Cable
Linker Script

## Slide 25: Library Generation Flow (in SDK)
Input files → MSS
  Output files → libc.a, libXil.a, libm.a
  Library generator is generally the first tool run to configure libraries and device drivers
    The MSS file defines the drivers associated with peripherals, standard input/output devices, and other related software features
  Library generator configures libraries and drivers with this information and produces an archive of object files:
    libc.a - Standard C library
    libXil.a - Xilinx library
    libm.a - Math functions library
Notes: Software Files
MSS
  An MSS file is supplied by the user as an input to the Library Generator (LibGen). The MSS file contains directives for customizing operating systems, libraries, and drivers
Linker script
  The linker script describes the mapping among all the sections in all the input object files and the output executable file. This file is used by the GNU linker
  Base System Builder will create a linker script for you
  If your address map specifies that the LMB, OPB, and external memory occupy contiguous areas of memory, you can use the BSB-created linker script to generate your executable
C/C++ source files
  Source code and header files written by the user

## Slide 26: Address Management
Embedded processor design requires you to manage the following:
  Address map for the peripherals
  Location of the application code in the memory space
    Block RAM
    External memory (Flash, DDR3, SRAM)
Memory requirements for your programs are based on the following:
  The amount of memory required for storing the instructions
  The amount of memory required for storing the data associated with the program

## Slide 27: Standard ARM Programming Model
Processing system and programmable logic look the same
  AMBA® and AXI interfaces
  Memory-mapped I/O
  Register access
Consistency for PS and PL = ease of use
Memory map usage: total of 4 GB
  1 GB: DDR RAM
  2 GB: dedicated to PL peripherals
  1 GB: PS peripherals, OCM, external flash

## Slide 28: Linker Script
Linker script controls the linking process
  Map the code and data to a specified memory space
  Set the entry point to the executable
  Reserve space for the stack
Required if the design contains a discontinuous memory space

## Slide 29: Linker and Locator Flows
.text1
.data1
.bss1
foo1.o
foo2.o
0xFFFF
0xF000
0xEFFF
0xEF00
0x0000
0x1FFF
0x2000
0xEEFF
Locate
Merged Output Sections
Unused
Executable Image
Code
uninitialized data
Initialized data
.text2
.data2
.bss2
Link
.text
.data
.bss

## Slide 30: Linker Script Generator GUI
Table-based GUI allows you to define the memory space for code and data sections
Launch from Xilinx Tools > Generate Linker Script, or from the C/C++ perspective, right-click on <project> > Generate Linker Script
The tool will create a new linker script (the old script is backed up)